Magnifier Pendant 6x/20D

MAG54

Please retain these instructions for future reference. These instructions are also available in other formats.

Contents

Importance of a low vision assessment	1

Choosing a magnifier	2

Warning! Important information	2

General description	2

Orientation	2

Aftercare	2

Effective lighting	3

Terms and Conditions of sale	3

# Importance of a low vision assessment

RNIB and Action for Blind People strongly advise anyone with visual impairment to have a low vision assessment. This is an NHS funded service usually accessed at your local hospital eye clinic or run by a local organisation. Referral to the clinic is usually by your General Practitioner (Doctor), Optometrist or Ophthalmologist. The assessment is free of charge and available to anyone with low vision. You do not have to be registered as sight impaired to access this service.

Low vision means that you will be finding it hard to see things as clearly as you would like to, even after you have had your eyes tested and are wearing the correct spectacles or contact lenses.

At the assessment a qualified low vision practitioner will check your vision and assess your suitability for low vision aids such as magnifiers. These clinics are usually able to provide at least one magnifier to you, free of charge. As magnifiers can be difficult to use initially, the practitioner will help you to get the best out of the equipment they prescribe. If you have been discharged by your eye specialist, you can ask your GP or Optometrist to refer you to the nearest clinic.

# Choosing a magnifier

RNIB's booklet 'Choosing your magnifier' is designed to help people with a visual impairment understand the various types of magnifier that can be used for specific tasks. This booklet is available from RNIB's Helpline in large print, audio or braille, or download from rnib.org.uk/magnifier

# Warning! Important information

Do not leave your magnifier in direct sunlight when it is not being used. The intensifying effect of the lens could become a fire hazard in direct sunlight. Use your protective cover (if provided) and always store in a safe place.

Never look at the sun directly through a magnifying lens as it could damage your eyes.

Do not look directly at the light source in illuminated magnifiers as LEDs are very bright.

Avoid impacting, banging or dropping your magnifier, as well as moisture and high temperatures which may cause damage.

Avoid putting your hands or fingers on the lens of your magnifier - always use the frame or handle.

# General description

Gold effect, gilt chain necklace with a 6x pendant magnifier attached. Pendant magnifiers are 'hand held' and should be used in the same way as standard hand held magnifiers. They are attached to a cord to hang around your neck for quick easy access when doing various activities, indoors and outdoors. Ideal for ‘spot’ reading such as in shops for seeing prices, they can be very discreet in public.

Magnification: 6x/20dpt

Circular Lens size: 40mm diameter

## Orientation

This magnifier comes supplied with a black leatherette protective case and small soft cleaning cloth. To protect the lens return to the storage bag when not in use. The chain has a small clasp, but the chain is large enough to place it over your head. The magnifier can be viewed from either side, both front and back. You will need to draw it close to your eye to get the best viewing area.

# Aftercare

Proper care of your magnifier means it will provide you with many years of untroubled reading. Clean the lens with a damp cloth (ideally a damp micro-fibre cloth). Never use solvents such as alcohol, benzene or other cleaning agents as these can damage the lens.

You may find small lines that look like hairline cracks at the edge of lightweight lenses or in the plastic frame. These are flow lines that occur during the production process, but they do not affect the function or durability in any way.

# Effective lighting

RNIB and Thomas Pocklington's booklet 'Make the most of your sight, improve the lighting in your home' demonstrates good practice by giving ideas, hints and tips. It explains how to light your home more effectively, as well as explaining different types of lighting and their benefits. It is available in large print, audio and braille from RNIB's Helpline or you can download it from our website.

# Terms and Conditions of sale

If you have not purchased the pendant magnifier directly from RNIB, please contact your retailer in the first instance.

This product is guaranteed from manufacturing faults for 12 months from the date of purchase.

You can request our full terms and conditions from RNIB Helpline on 0303 123 9999. They are also available at rnib.org.uk/shop

Helpline, RNIB, PO Box 173, Peterborough PE2 6WS, U.K.

Email UK: shop@rnib.org.uk

Email for international customers: exports@rnib.org.uk

Textphone: 0845 758 5691

Registered charity No. 226227

Written May 2011