User and Installation instructions

For

ORTHROS dual joystick one handed controller

“Squiddy for PS3-SAP” version

Please read these instructions for installation and use before attempting to use this product.

These instructions have been prepared in order that the product is not used outside of its limitations, and to ensure the user obtains maximum satisfaction from its use.

# CONTENTS

FRONT SHEET	PAGE 1

CONTENTS PAGE	PAGE 2

1	INTRODUCTION	PAGE 2

2	LIMITATIONS OF USE	PAGE 2

3	WARNINGS	PAGE 3

4	DESCRIPTION OF UNIT	PAGE 3

5	OPERATING INSTRUCTIONS 	PAGE 3
6	PROBLEM SOLVING	PAGE 4

7	CLEANING INSTRUCTIONS	PAGE 4
8	TECHNICAL SPECIFICATION 	PAGE 4
End of document	PAGE 4

1	INTRODUCTION

This manual provides the necessary information for the use of the handset, and provides basic fault finding information. The unit is identified by the information on the labelling on the unit, and includes: Type, Year of manufacture and Serial Number. The system is classed as an accessory to a “Medical Device” for the purposes of the European Medical Devices Directive 93/42/EEC 14th June 1993, as it compensates for an injury or handicap.

The purpose of the device is to allow one handed access to the features and functions of the SONY Playstation. This is achieved by connecting the device to a LEPMIS “Squiddy” switch expander, which then connects to a LEPMIS PS3 Switch Access Pod. accessories manufactured by LEPMIS or other approved manufacturers can be connected to the LEPMIS PS3 Switch Access Pod.

- LIMITATIONS OF USE

The unit is reasonably well protected from the effects of dust, water and EMI, but there are no particular features to prevent water entering the unit. Do not soak the unit or attempt to “wash” it in any way. Clean sparingly with a barely damp cloth and mild detergent if really necessary.	The unit is intended to be used in a home or school environment, and due to its lack of full environmental protection, must not be subjected to exposure to the elements. The unit is rated for continuous operation but you are advised to consult the SONY Playstation documentation on the length of time the unit should be used or how long the SONY console should be left ON. Operating temperature range, as per the SONY PS3 operating instructions.

This unit MUST NOT be used to control a mobility device, for example a wheelchair.

# WARNINGS

# No unauthorised access or dismantling of the unit allowed. Authorisation will only be given by the manufacturers – LEPMIS,  in writing, to competent persons.	It is not recommended that you play any sort of computer game for extended periods of time. Playing computer games can become an addictive habit, leading to emotional and physical changes to the player.	

USE YOUR PLAYSTATION SENSIBLY !

4	DESCRIPTION OF UNIT

This unit consists of a plastic enclosure as in the picture on the front page, which houses  simple circuit boards with joysticks and switches.

The main feature of this controller is that the SHAPE buttons are duplicated on both sides of the unit for use by either left or right handed persons.  It should be noted however that the standard configuration is for the right hand lower three buttons to actually perform the functions of the SYSTEM buttons, - Start, Select and PS. See the diagram below.	









Using the Squiddy switch expander in conjunction with the PS3-SAP, ALL of the switch functions can be re-configured to achieve any switch action pattern that is desired. It is quite simple therefore to swap the Start, Select and PS leads for the Box, Ex and Circle leads to change from right to left hand use.

The Shoulder buttons, L1, L2, R1, R2, are implemented on the back spine of the handset, and are labelled up as per the format of the PS3-SAP and “Squiddy” expansion box.

The bottom joystick is normally configured to the Left hand joystick of a standard controller. And the top the right.  NOTE:  Using the Squiddy  switch expander, the bottom joystick can be configured to function in either “Push” or “Tilt” mode, depending on the users particular preference. A small switch on the left hand side of the Squiddy expander makes this selection.  All other switch actions are as the standard SONY handset. Rumble is not currently implemented on the ORTHROS controller.

5	OPERATING INSTRUCTIONS

Plug the Orthros Joystick) into the socket on the right hand side of the unit “Squiddy” switch expander interface. Plug the jack plugs and D connectors into their corresponding sockets on the PS3-SAP.  Follow the instructions for the “Squiddy” interface and the PS3-SAP.

This symbol       	means that the ORTHROS controller must be re-cycled when no longer required. Please do not throw away in the general refuse. Please request from LEPMIS a pre paid envelope in which to return it to the manufacturers.

6	PROBLEM SOLVING

Common faults such as the switches or joysticks working intermittently will arise due to wear and tear. Jack sockets will degrade from repeated connection and disconnection of the plugs. This is unavoidable but the sockets should last a number of years before they need replacing. 

Please contact your supplier of this unit for repairs or maintenance. Failing that, contact LEPMIS whose address and telephone number are listed on the last page of this user manual.

7 	CLEANING INSTRUCTIONS

When necessary, the unit should be cleaned with a barely damp cloth, using only a tiny amount of household detergent. DO NOT USE abrasive products or solvents.	 

AVOID getting fluids or foreign material into the sockets as they will either corrode or become jammed up, and stop working. Failure of the sockets in this way is not covered by the warranty.

# 8	TECHNICAL SPECIFICATION

Size:		10.5cm wide,  by 5.5cm deep, by 18cm high, (not including cable)

Weight:		0.51 kg

Operating Voltage		No internal power supply. Do not exceed 12v

This User / Installation manual has been written for the:-

LEPMIS  “ORTHROS” Dual Joystick controller, for the  “Squiddy” Expansion Adapter.

# which is designed to meet the general requirements of:-

the Medical Devices Directive 93/42/EEC  14 June 1993.

and conforms to the requirements of BSEN 60529 to a level of IP30

Supplied by:

# Long Eaton Powered Mobility Integration Service

# 24 Laurel Crescent

# Long Eaton

# Nottingham

# NG10 3NN

# Tel:				0771  495 8061

# e-mail:				Support@LEPMIS.co.uk

# On the WEB, at 	LEPMIS.co.uk

# We hope you enjoy the use of this product, but please do so safely!

# End of Document

# Text boxes

PS

Long Eaton Powered Mobility Integration Service

Unique Solutions for Unique People

Integrated Systems for an Integrated Life Style

Select

Start